## Slide 1: CS111: Operating Systems Principles
Lab 4 A B and C
Vishwas Suryanarayanan

## Slide 2: Lab 4: BeagleBones, Sensors and Security!
Full Description (look under the folders for P4[A B C]:
  https://web.cs.ucla.edu/classes/winter19/cs111/labs/
Additional Setup:
  Need a BeagleBone
Warning:
  Servers get overwhelmed with requests towards the end of the week (as deadlines approach)
    Do not wait till the last minute to test Lab 4C!!!

## Slide 3: Lab 4A: Setting up your BeagleBone
Step 1: Connect BeagleBone to the computer over USB
Step 2: Install Drivers (Windows/MacOSX) – optional?
Step 3: Connect to the BeagleBone over SSH on USB
  192.168.7.2
But what if you have not yet flashed it?
  Download image: https://beagleboard.org/latest-images
  Download etcher: https://www.balena.io/etcher/
  Burn image onto MicroSD card
  Insert card, hold down USER/BOOT and power it up
  Open the linux partition, /boot/uEnv.txt and uncomment flasher line, and reboot.
  Wait impatiently, tapping your foot.

## Slide 4: Connecting to WPA2-PSK Networks
Utility: connman
  > enable wifi
  > scan wifi
  > services
  > agent on
  > connect “service”
Run:
  $ ifconfig:
    To see IP Address assigned

## Slide 5: Connecting to `eduroam`
Open: /var/lib/connman/eduroam.config
Add:
  [global]
  Name=eduroam
  Description=configuration for eduroam
  [service_eduroam]
  Type=wifi
  Name=eduroam
  EAP=peap
  Phase2=MSCHAPV2
  CACertFile=/etc/ssl/certs/AddTrust_External_Root.pem
  Identity=username@ucla.edu
  Passphrase=**********
Restart: wpa_supplicant, connman.service
Connect!

## Slide 6: Change hostname
Step 1: Use the hostname command
  sudo hostname `host_name`
Step 2: Edit the /etc/hostname file
  sudo cat > /etc/hostname
  `host_name`
  ^D
Step 3: Associate loopback with hostname in /etc/hosts
  Hint: Use sudo vim /etc/hosts

## Slide 7: Other things to do
Install git via apt-get
  sudo apt-get install git
Use scp/sftp to copy a source file into the beaglebone
Connect to the beaglebone over SSH and build and run the source file.
Take screenshots and selfies!

## Slide 8: Lab 4B: Sensors!
Use: MRAA library functions (NOT Grove Library functions)
Attach the Grove Base Shield on top.
Attach:
  Grove Button to GPIO_50 (MRAA pin #60)
  Grove Temperature Sensor to Analog A0/A1 connector (MRAA pin #1)
Sample temperature from the sensor
Create a single line report per sample and write to STDOUT
AIO functions
GPIO functions

## Slide 9: poll (2)
Include:
  poll.h
Function call:
int poll(struct pollfd *fds, nfds_t nfds, int timeout);
Used to: wait for a set of file descriptors to become ready for IO
struct pollfd {int fd; short events; short revents; }
Events:
  POLLIN
  POLLOUT
  POLLERR
  POLLHUP
Useful to poll input from STDIN while not blocking

## Slide 10: fcntl
Can be used to tinker around with file descriptors
Function:
int fcntl(int fd, int cmd, ... /* arg */ );
Important command:
  F_SETFL: Sets the file descriptor flags.
  Why do we need it?
  O_ASYNC
TLDR: fcntl can be used to set the O_ASYNC flag for a file

## Slide 11: Quick Intro to MRAA
Include: “mraa.h”
Compile and link with -lmraa
No need to install MRAA: Should be pre-installed on the Bones.
Don’t use the Grove Libraries!
Try: Printing mraa_get_version()

## Slide 12: AIO functionality with MRAA
Step 1: Initialize.
Step 2: Read values (Or set values)
Step 3: Close
(Sensor values are floating point values that correspond to ?)
/* initialize AIO */
aio = mraa_aio_init(AIO_PORT);
if (aio == NULL) { fprintf(stderr, "Failed to initialize AIO\n");
mraa_deinit(); return EXIT_FAILURE; }
while (flag) { value = mraa_aio_read(aio);
float_value = mraa_aio_read_float(aio);
fprintf(stdout, "ADC A0 read %X - %d\n", value, value);
fprintf(stdout, "ADC A0 read float - %.5f\n", float_value);
}
/* close AIO */
status = mraa_aio_close(aio);
if (status != MRAA_SUCCESS) {goto err_exit;}

## Slide 13: GPIO Functionality with MRAA
Create a context and initialize: mraa_gpio_init(PORT);
Set port to be an INPUT/OUTPUT port: mraa_gpio_dir(port, DIR)
Read/Write from/to port: mraa_gpio_write(port, level);
Close the port: mraa_gpio_close(port)
GPIO_50: MRAA port 60.
AIN0 pin: 1
Button -> Use an Interrupt.
  On rising edge/falling edge?
  mraa_gpio_isr(button, MRAA_xyz, &function, args)

## Slide 14: Temperature Reading Algorithm
B (value of thermistor – 4275)
R0 (100kOhm)
R = R0*(1023/V - 1 )
temperature = 1.0/(log(R/R0)/B+1/298.15)-273.15
Where did all these numbers come from??
What scale is this in???

## Slide 15: Lab 4C: Security
Why do we care?
What could go wrong?
They’re just devices – why would anyone hack them?
How is it any different from hacking a computer?
What are we supposed to do for this lab?
  Ping the TLS server to see if it’s up (lever.cs.ucla.edu)
  Talk to the logging server
  Talk to the TLS server over SSL
Review the OpenSSL documentation

## Slide 16: Logging without encryption – Introduction to Socket Programming
Socket: An endpoint (IP Address + port) that identifies a process on a network.
To connect to a server, we need to know:
  IP Address (or ?)
  Port
Step 1: Resolve hostname to IP address. How? DNS!
Step 2: Create a (client) socket
Step 3: Connect to server socket
Step 4: Write to server socket
Step 5: Close socket

## Slide 17: gethostbyname
Library includes:
  #include <sys/socket.h>
  #include <netinet/in.h>
  #include <netdb.h>
Function call:
  struct hostent *gethostbyname(const char *host);
Structure definition:
  struct hostent { char *h_name; char **h_aliases, int h_addrtype, int h_length, char **h_addr_list, char *h_addr};

## Slide 18: socket API
Need server socket details:
  struct sockaddr_in {
  short sin_family; // e.g. AF_INET, AF_INET6
  unsigned short sin_port; // e.g. htons(3490)
  struct in_addr sin_addr;
  char sin_zero[8]; // zero this if you want to
  };
Call socket!
  int socket(int family, int type, int protocol)
Connect to the server!
  int connect(int sockfd, &server, sizeof(server))
Send messages!
  int send(sockfd, “MESSAGE”, length_of_message)
Close the socket

## Slide 19: Logging over SSL

## Slide 20: Procedure for Logging over SSL
Step 1: Initialize Library
  SSL_library_init()
  SSL_load_error_strings()
  OpenSSL_add_all_algorithms()
Step 2: Create a new context
  SSL_CTX *context = SSL_CTX_new(TLSv1_client_method())
Step 3: Create an SSL client
  SSL *client = SSL_new(context);
Step 4: Associate file descriptor with SSL
  What file descriptor?
  SSL_set_fd(client, fd)
Step 5: Connect
SSL_connect(client)
Step 6: Write
SSL_write(client, “message”, 8)
Step 7: Shutdown and Free
SSL_Shutdown(client); SSL_free(client);

## Slide 21: Any Questions?
Next week: Final review: bring your questions!